## Slide 1: Navigation Method for VTOL Type UAV using a Limit-cycle Navigation Method and Fuzzy Logic Control
Byung-Cheol Min
Kyung Hee University
(Thesis Advisor : Prof. Donghan Kim)

## Slide 2
Introduction
Introduction
Path Planning Algorithm
UAV (Unmanned Aerial Vehicle)
Path Tracking Method
Conclusion
Contents

## Slide 3: - What is a navigation method?
Navigation
Path Planning
Path Tracking
(c) Commercial Airplanes
(a) Unmanned Aerial Vehicles
(b) Unmanned Ground Vehicles
1. Introduction
Introduction
- Applications

## Slide 4: Classic Path Planning Approach
- Potential Field Method
- Limit-cycle Navigation Method
(d) Simulation on the Limit-Cycle navigation method
(b) r = 50
(c) r = 70
(a) r = 30
1. Introduction
Introduction

## Slide 5: The Basic Concept of Limit-cycle method in three dimensions (3D)
dz
dx
dy
Dh
dx = current x position – obstacle x position
dy = current y position – obstacle y position
dz = current z position – center of the obstacle z position
center of the obstacle
current position
Δh
Δy
Δx
Dh is a tangent line between the current position and the tangent point of an obstacle circle.
With this obtained angle, the input of the z-value can be calculated as
Δx and Δy values are obtained by the original limit-cycle navigation method.
Path Planning Algorithm
2. Path Planning Algorithm

## Slide 6
(a) unsuitable path
(b) possible paths
(c) unsuitable path
(d) suitable path
Although the proposed method verified a variety of merits in 3D, it also showed several drawbacks.
1. The method usually draws the path with setting previous along the center of obstacle’s height, depicted in (a).
2. The method generates the path only by avoiding to the side of the obstacle, depicted in (c).
Problem Statement
2. Path Planning Algorithm
Path Planning Algorithm

## Slide 7
Put the initial point for Pi and
the destination point for Pd
Render the obstacle
Draw a line P(t) between Pi and Pd
START
Ray
Tracing
Path
Planning
Ray tracing is
an algorithm that shoots beams of light to determine the accurate location and the size of the objects.
In this paper, however, the method is used for the aircraft to find the shortest path to reach the destination while avoiding the obstacle.
Path Planning Based on the Methods of Ray Tracing and Limit-Cycle
2. Path Planning Algorithm
Path Planning Algorithm

## Slide 8
Put the initial point for Pi and
the destination point for Pd
Render the obstacle
Draw a line P(t) between Pi and Pd
Does two Intersections exist?
Generate a straight path
START
Ray
Tracing
Path
Planning
Yes
No
END
Eq. (1) can be expressed as
The coefficients a, b, and c in Eq. (2) can be expressed as follows.
By solving the discriminant, we can know whether the line P(t) intersects the sphere or not.
(1)
(2)
(3)
Path Planning Based on the Methods of Ray Tracing and Limit-Cycle
2. Path Planning Algorithm
Path Planning Algorithm

## Slide 9
Put the initial point for Pi and
the destination point for Pd
Render the obstacle
Draw a line P(t) between Pi and Pd
Does two Intersections exist?
Decide the path between a horizontal direction and a vertical direction
START
Ray
Tracing
Path
Planning
Yes
No
END
(b) x-y plane, z=0
(c) x-z plane, y=0
(a) line P(t) from Pi to Pd
Generate a straight path
When the horizontal direction is chosen, limit cycle is generated on the x-y plane.
When the vertical direction is chosen, limit cycle is generated on the x-z plane.
Path Planning Based on the Methods of Ray Tracing and Limit-Cycle
2. Path Planning Algorithm
Path Planning Algorithm

## Slide 10
Only slight difference occurs between the hypothetical limit cycle in 3D and the proposed limit cycle in 2D.
The huge gap occurs if the radius of limit cycle is calculated based on the center of the obstacle.
Put the initial point for Pi and
the destination point for Pd
Render the obstacle
Draw a line P(t) between Pi and Pd
Does two Intersections exist?
Decide the path between a horizontal direction and a vertical direction
Calculate a radius of the limit cycle
based on the line
Generate a path by limit cycle
START
Ray
Tracing
Path
Planning
Yes
No
END
Generate a straight path
Path Planning Based on the Methods of Ray Tracing and Limit-Cycle
2. Path Planning Algorithm
Path Planning Algorithm

## Slide 11
Two suitable paths were generated among numerous paths that can be planned by limit cycle method.
And then, the shortest path was decided by comparing two distances depicted as a solid line.
82.43 m
89.1 m
Simulation Result 1
(a)
2. Path Planning Algorithm
Path Planning Algorithm

## Slide 12
Simulation Result 2
(a)
(b)
2. Path Planning Algorithm
The three paths from different initial points is successfully generated.
There are no gaps between the sphere and three paths. Thus, each of paths is smooth enough for UAVs to fly because of limit cycle characteristics.
Path Planning Algorithm

## Slide 13
Path Planning for Dynamic Obstacle Avoidance: collision detection method
(a)
2. Path Planning Algorithm
(1) Velocity vector
(2) Position of moving object
(3) Calculate the time t whenthe distance d
between P(t) and O(t) equals to rP + rO
An algorithm to generate a path to avoid dynamic obstacles is mainly comprised of a collision detection method and standard rules of airplane traffic.
Path Planning Algorithm

## Slide 14
2. Path Planning Algorithm
“If both airplanes approach from opposite sides, they are supposed to give way by turning right away from each other to avoid a collision, and if flying airplanes come into conflicting paths side by side, the left airplane turns right to yield.”
Path Planning for Dynamic Obstacle Avoidance: standard rules of airplane traffic
“Right of way” of Federal Aviation Regulation (FAR) 91.113 to collision avoidance
“Rules of the air” of the International Civil Aviation Organization (ICAO) annex 2
In case there are more than two UAVs in the same operation area, standard rules to control their traffic are necessary.
Path Planning Algorithm
Notes: 국제민간항공기구 부속서 2권의 , 미국연방항공규칙 91.113의

## Slide 15
Collision Detection Method
(b)
2. Path Planning Algorithm
Similarly, we set up the standard rules of airplane traffic as follows:
If two UAVs approach from opposite sides (i,e., more than 90 degrees), the UAV is supposed to give way by turning right away from the moving obstacle to avoid a collision.
Path Planning Algorithm

## Slide 16
Standard Rules of Airplane Traffic
(c)
2. Path Planning Algorithm
If the dynamic obstacle comes into conflicting the UAV's path within less than 90 degrees, the UAV waits for a while to yield.
Path Planning Algorithm

## Slide 17
Simulation Result 3
(a)
2. Path Planning Algorithm
the angle between the moving direction of the UAV and the obstacle was set for bigger than 90 degrees.
The path was generated at the predicted position of a collision (42, 52) with the supposition that an obstacle exists at that position.
Path Planning Algorithm

## Slide 18
Common UAV Configurations
Fixed-wing Type
Vertical Take-Off and Landing Type
(VTOL Type)
Configuration | Picture | Application | Advantages & Drawbacks
fixed-wing (Predator) |  | military reconnaissance combat | - high endurance flights silent no hovering
single (Fire Scout) |  | meteorology research reconnaissance | good controllability and maneuverability - complex mechanics - large rotor
coaxial rotors (Airscooter) |  | -research -surveillance | - compactness simple mechanics complex aerodynamics
quad rotors (DraganFlyer) |  | -research -surveillance | - good maneuverability Increased payload - high energy consumption - large size
UAV
3. UAV(Unmanned Aerial Vehicle)

## Slide 19
(a) Hovering configuration
(b) Pitching & rolling configuration
(c) Yawing configuration
F1(0) + F2 (0) + F3 (0) + F4(0) =
For a hovering flight, the four driven forces are
Basic Principles of the Quad-rotor UAV
3. UAV(Unmanned Aerial Vehicle)
UAV

## Slide 20
1) The rotational transformation matrix between the earth-frame {E} and the body frame {B}
2) Equations of the translational motion in the earth frame are derived by the Newton’s laws
(a) The coordinate system with an earth frame {E} and a body frame {B}
The Dynamic Modeling of the Quad-rotor UAV
3) Resultant equations of motion as follows
4) Control inputs of the model
3. UAV(Unmanned Aerial Vehicle)
UAV

## Slide 21
(b) The path tracking scheme
(a) Typical Fuzzy Logic Control (FLC)
Fuzzy Logic Control
Path Tracking Method
4. Path Tracking Method
To control thrust and attitude of the VTOL Type UAV, which mostly affect its position, fuzzy logic control (FLC) is proposed.
The FLC, which is activated after generating the path, will be in charge of controlling the overall system of the quad-rotor UAV so that it can move to any desired position effectively.

## Slide 22
Nine Fuzzy Logic Controllers (FLCs) were used to handle nonlinear system.
Fuzzy Logic Control
4. Path Tracking Method
Path Tracking Method
e/Δe | NB | NM | NS | ZO | PS | PM | PB
NB | NB | NB | NB | NB | NM | NS | ZO
NM | NB | NB | NB | NM | NS | ZO | PS
NS | NB | NB | NM | NS | ZO | PS | PM
ZO | NB | NM | NS | ZO | PS | PM | PB
PS | NM | NS | ZO | PS | PM | PB | PB
PM | NS | ZO | PS | PM | PB | PB | PB
PB | ZO | PS | PM | PB | PB | PB | PB

## Slide 23
(a) The traces of path tracking by the quad-rotor UAV while ascending using FLC.
(b) The each velocity ratio of x-y-z axes per time axis based while the quad-rotor UAV is ascending.
(c) The each position of x-y-z axes per time axis based while the quad-rotor UAV is ascending.
Simulation Result 1
4. Path Tracking Method
Path Tracking Method

## Slide 24
(d) The traces of path tracking by the quad-rotor UAV while descending using FLC.
(e) The each velocity ratio of x-y-z axes per time axis based while the quad-rotor UAV is descending.
(f) The each position of x-y-z axes per time axis based while the quad-rotor UAV is descending.
Simulation Result 2
4. Path Tracking Method
Path Tracking Method

## Slide 25
(a) The result of a simulation on the proposed navigation method: There are three different initial positions and the same destination. ‘’ indicates way points from the initial position of the UAV to its destination.
Simulation Result 3
4. Path Tracking Method
Path Tracking Method

## Slide 26
(b) An enlarged portion of the problem of path tracking.
Problem with Simulation Result 3
(c) The each velocity ratio of x-y-z axes per time axis based while the quad-rotor UAV is flying toward the destination. There is a problem that the UAV repeats stop-and-go at regular intervals.
4. Path Tracking Method
Path Tracking Method

## Slide 27
Method to Solve the Problem with Simulation Result 3
Spheres centered at the way points are drawn in the form of ,where x, y, and z represent the position of the way point (desired position), and i means the order of way points, and r means a radius of sphere.
When the UAV passes the ith sphere, the current desired position (xi, yi, zi) is changed to the following desired position (xi+1, yi+1, zi+1).
4. Path Tracking Method
Path Tracking Method

## Slide 28
(a) The result of a simulation on the new path tracking solving the problem that the UAV repeats stop-and go around the way points
Simulation Result 4
4. Path Tracking Method
Path Tracking Method

## Slide 29
(b) An enlarged portion of the simulation result
Simulation Result 5
(c) The each velocity ratio of x-y-z axes per time axis based while the quad-rotor UAV is flying toward the destination
4. Path Tracking Method
Path Tracking Method

## Slide 30
(a) The result of dynamic obstacle avoidance in a case where the obtacle comes into a conflicting the UAV's path within less than 90 degree
Simulation on Dynamic Obstacle Avoidance: the Second Standard Rule of Airplane Traffic
(b) Dynamic Obstacle Avoidance: the Second Standard Rule of Airplane Traffic
4. Path Tracking Method
Path Tracking Method

## Slide 31
Simulation on Dynamic Obstacle Avoidance: the Second Standard Rule of Airplane Traffic
(a) Obstacle
(b) UAV
(c) The each position of the UAV
4. Path Tracking Method
Path Tracking Method

## Slide 32
Extension of the original limit-cycle navigation method of three dimensional spaces
New path planning algorithm based on the methods of ray tracing and the extended limit-cycle navigation method
Algorithm comprised of a collision detection method and standard rules of airplane traffic that generates a path to avoid collisions with dynamic obstacles
Fuzzy logic control method in order for the UAV to converge quickly on the desired position
Solving the problem that the UAV repeats stop-and go around the way points, using virtual spheres
Conclusion
5. Conclusion

## Slide 33
function [x, y, z] = limtcycle(Pos_x, Pos_y, Pos_z, ObPosx , ObPosy, ObPosz, r, direct)
dx = (Pos_x -ObPosx);
dy = (Pos_y -ObPosy);
dz = (ObPosz - Pos_z);
Dh = sqrt(dx^2 + dy^2);
if(direct == -1)
ddx = -dy*r^2 + dx * (r^2 - dx^2 - dy^2);
ddy = dx*r^2 + dy * (r^2 - dx^2 - dy^2);
else
ddx = dy*r^2 + dx * (r^2 - dx^2 - dy^2);
ddy = -dx*r^2 + dy * (r^2 - dx^2 - dy^2);
end
theta_xy = atan2(ddy,ddx);
Theta_z = atan2(dz,Dh);
Del = 5;
Del_x = Del*cos(theta_xy);
Del_y = Del*sin(theta_xy);
Del_h = Del*tan(Theta_z);
x = Del_x + Pos_x;
y = Del_y + Pos_y;
z = Del_h + Pos_z;
end
Limit-cycle Matlab Source

## Slide 34
Publications - 5 Journal Publications, 5 Conference & Symposium Proceedings
- Journal Publications
B.C. Min, and D.H. Kim, “A Navigation Method for VTOL type UAV Using Limit-cycle Navigation Method and Fuzzy Logic Control," IEEE Transactions on Systems, Man, and Cybernetics, 2010. (in preparation)
B.C. Min, M. Kim, and D. Kim, "Fuzzy Logic Path Planner and Motion Controller by Evolutionary Programming for Mobile Robots," International Journal of Fuzzy Systems, Vol. 11, No. 3, September 2009.
B.C. Min, D. Kim, Y.H. Kim, K.Y. Kim, and C. Park, "Development of Violin Self-Training Algorithm Using Fuzzy Logic," Journal of Korean Institute of Intelligent Systems, Vol. 19, No. 4, August 2009. (in Korean)
B.C. Min, C.H. Cho, K.M. Choi, and D. H. Kim, "Development of a Micro Quad-Rotor UAV for Monitoring an Indoor Environment,", Lecture Notes in Computer Science (LNCS), FIRA CIRAS 2009, Vol. 5744, pp. 262-271, August 2009.
C.H. Cho, B.C. Min, and D. H. Kim, "A Gait Generation for an Unlocked Joint Failure of the Quadruped Robot with Balance Weight," Lecture Notes in Computer Science (LNCS), FIRA CIRAS 2009, Vol. 5744, pp. 251-261, August 2009.
- Conference & Symposium Proceedings
B.C. Min, H.Y. Kwon, and D.H. Kim, "Path Planning Algorithm for VTOL Type UAVs Based on the Methods of Ray Tracing and Limit Cycle," IEEE International Symposium on Computational Intelligence in Robotics and Automation (CIRA 2009), December 2009.
B.C. Min, E.J. Lee, S.H. Kang, and D.H. Kim, "Limit-cycle Navigation Method for a Quad-rotor Type UAV," Industrial Electronics, 2009. ISIE 2009, IEEE International Symposium on, pp. 1352-1357, July 2009.
S.H. Kang, B.C. Min, C.H. Cho, S.Y. Nam, and D.H. Kim, "The Position Control for Three Wheel Omni-directional Mobile Robot Using FLC," IEEK Summer Conference 2009, Vol. 32, No. 1, pp. 691-692, July 2009. (in Korean)
Y.W. Lim, B.C. Min, J.W. Kim, S.Y. Nam, and D.H. Kim, “Local-Path Planning Using the Limit-cycle Navigation Method Applied to the Edge of an Obstacle with the Edge Detection Method”, International Conference On Electronics, Information, & Communication (ICEIC 2010), April 2010.
Y.H. Kim, J.W. Kim, B.C. Min, and D.H. Kim, “Dynamic Obstacle Avoidance Using Vector Function Algorithm”, International Conference On Electronics, Information, & Communication (ICEIC 2010), April 2010.